HD IPTV SET TOP BOX

USER MANUAL

2010

1．Remote-control declaration：

The latest STB remote diagram after April,6th,2010. The latest version operates according to this remote diagram now.

二：STB set：

一、connect the power，menu will appear after lanuching.

After about 30 seconds it will enter into tacity approve EPG address, press down “set up”and then appears “HD BOX seting” loading interface(As shown in figure)

Entry the default code 123456and find “set HD BOX seting”interface.（as following）：Basic Setting version

note：

is   MAC   adress

is vension number

base setting

、declaration：

- language

install STBstarting language（mainly Chinese and English）.

- COOKIES

Save username and code(if choose “yes”，clear away the autosave VOD account number andcode).

- Set basic Password

Set login “set HD BOX seting”interface code

- Confirm Password

Confirm the password on the basic of the password is correct or not

- Load Default Setting

Recovery all default seting of set HD BOX seting of factury(ebcept expert seting epg address)

3.Video setting

1、press  (Ch–)▼ button  at set HD BOX seting interfac，button，enter in video seting

2、TV standard：

- television system（system）

set STB output system：PAL、NTFS、HD720_50HZ、HD720_50HZ 、HD1080_50HZ 、HD1080_60HZ、HD1080_24HZ、SVGA800×600

- screen ratio

set play menu ‘s reveal ratio：16：9 、LB4：3、PS4：3、

- Brightness

Adjust the the TV color   0-100

- contrast ratio

adjust tthe contrast ratio of interface: adjustable 0-100

- Channel Select of Audio

Set the sound broadcast files playback modes: stereo, left, and right track channels

- Digital  output

4.Network setting

1、press (Ch–)▼  at set HD BOX seting,enter into Network setting.

1Access Mode: select Static

2  DHCP: Here select” NO”

if select “yes”， then the system get IP address automatically；if”no”，that need seting  the IP address ,So set IP address manually, EPG. Can display after getting IP address.

3 IP address: set STB internet IP address

FLV IP Flesh Encoder need seting the IP address by hand, so select :NO”, try to make every network IP address similar

For example: IP Net work IP address: 192.168.1.101

Set top box 1         192.168.1.1

Set top box 2         192.168.1.2

Set top box 100       192.168.1..100

Set top box 1000      192.168.2.200

IP flesh Encoder 1     192.168.1.101

IP flesh Encoder 2     192.168.1.102

IP flesh Encoder100    192.168.1.201

4 Net mask: Set STB subnet .mask, the system can get it automatically

5 Gateway: fatory default

6 DNS Server

Here select” Auto”to get DNS automatically

if select “Auto”， then the system get DNS address automatically；if “no”，then need  set DNS address  manually

7 Primary DNS Server: factory default

8 Secondary DNS Server: factory default

Save  the above seting

5.Advance setting

1、 press (Ch–)▼button  at set HD BOX seting,，enter into Advance setting

2、input code（defult code is 123456）, press “OK”，enter into Advance setting。

- 1 EPG Type ：Select ”RTMP”

EPG type  :PAGE  MMS  UDP  RTSP  RTMP  HTTP  HTTPS (PAGE is the web adress of starting up；other waysis to  fill video of original flow address，That is the direct broadcast on the corresponding video)

2 EPG Address :

Select opposite EPG type and put in opposite flow address。

(for example：select EPG Type: RTMP ,EPG Address change into RTMP://。Inout address 192.168.1.102/live/myvideo,(program name can seting in IP encoder software)，That is the direct broadcast on the corresponding video)（presention：If access interface appear white interface and interface with a garbled because no access IP box, choose to enter setup goal setting IP Network inside can be displayed）)

- Upgrate address：

Input the FTP server address after the upgrade automatically restart automatically preserve box to upgrade to the latest version。

note：Upgrade process absolutely cannot fail, or may be damaged, but it happened STB manufacturer, please contact problem of after-sales service

4 Advanced Password

Set into the senior set password

5 Confirm Password

Confirm the password on a set of advanced set password is correct or not

- Boot Mode : EPG

Modify saved all the recovery of senior Settings。

6.System upgrade

1、press (Ch–)▼ button at set HD BOX seting，enter  system setting

station：

- Internet upgrate

Network upgrades modes (manual, automatic)

Manual or automatic major difference whether the new version system upgrade, choose "automatic" automatic detection system version of the new version of the new automatic update, Choose "manual" system that will appear in a new version is that the new version update tip

- USB upgrate

The upgrade file save to u disk, files in directory, then u were the USB plug into the USB interface box tail, USB upgrade (upgrade under USB)! Choose "Upgrade button (Upgrade)" save Settings, system in 5 seconds after the restart automatically Upgrade automatically. (if you save Settings for 10 seconds after hasn't hair should restart again into electricity, and the interface resetting!

- Manual upgrate

- method：easiest way：recommended

一：Img. The upgrade install via USB copy to U disk, mobile hard disk or should be stored in a file (root directory is: the root directory)。

二：connect all the line of stb, power temporarily shut up, and in the power of the state, the box with the upgrade file USB plug to the USB port of STB.

三：After all, hold to the front panel OK button box, and then open source, STB, OK button on continuously according to 10 seconds later can loosen, please wait, this picture in the picture, welcome in the picture, after entering upgrade automatically upgrade, the remaining set-top box after a few minutes, STB upgrade automatically restarts.

Four: the upgrade is complete, the first computer, will open a blank page, because all the parameters are all manufactured Settings, STB without any data, including IP address is the default setting, customer first need to manually, convenient to set the IP network access to box. According to the operation, control setup, password and press ok, choose 123456 left navigation Network: the third goal, click ok button. If the customer network environment is the use of dynamic DHCP assign IP, default has chosen DHCP, as long as the users' choice of preservation "below. If is manual IP, can choose manual, and set the IP address below, the subnet mask, nets, preferred DNS. According to save.

Similarly, can install STB access to address the EPG, STB access.

八、broadcast Uflash drive file

1.we now discuss  how mass broadcasting U disk, mobile hard disk in the video.

First the external storage equipment receiving STB, through the USB port, the system automatically after the power into the original setting good EPG address, press the remote U/HDD (the second, the third button can enter the local document interface. Through the key choose folder, click ok to play video,. Broadcast time, can press, and etc. According to stop return to play browsing interface

2、bove all the navigation: audio, images, video. Can be classified according to the navigation. You need to select the files play

note：The remote LIVE temporarily defined role, such as during a visit to refresh the EPG, can refresh the page。

Noted: after finished the STB seting , Please turn off the STB and Turn on again, the STB will search the program automatically